/* Default linker script, for normal executables */
OUTPUT_FORMAT("elf32-msp430")
OUTPUT_ARCH("msp430")

/* INCLUDE memory.x begin */
MEMORY {
  sfr : ORIGIN = 0x0000, LENGTH = 0x0010 /* END=0x0010, size 16 */
  peripheral_8bit : ORIGIN = 0x0010, LENGTH = 0x00f0 /* END=0x0100, size 240 */
  peripheral_16bit : ORIGIN = 0x0100, LENGTH = 0x0100 /* END=0x0200, size 256 */
  bsl : ORIGIN = 0x1000, LENGTH = 0x0400 /* END=0x1400, size 1K as 1 1024-byte segments */
  ram (wx) : ORIGIN = 0x2000, LENGTH = 0x1000 /* END=0x2400, size 4K */
  rom (rx) : ORIGIN = 0xc400, LENGTH = 0x3b80 /* END=0xff80, size 15K */
  signature : ORIGIN = 0xff80, LENGTH = 0x0008 /* END=0xff88, size 8 as 1 8-byte segments */
  vectors : ORIGIN = 0xff80, LENGTH = 0x0080 /* END=0x10000, size 128 as 64 2-byte segments */
  /* Remaining banks are absent */
  infomem : ORIGIN = 0x1800, LENGTH = 0x0200
  infoa : ORIGIN = 0x0000, LENGTH = 0x0000
  infob : ORIGIN = 0x0000, LENGTH = 0x0000
  infoc : ORIGIN = 0x0000, LENGTH = 0x0000
  infod : ORIGIN = 0x0000, LENGTH = 0x0000
  ram2 (wx) : ORIGIN = 0x0000, LENGTH = 0x0000
  ram_mirror (wx) : ORIGIN = 0x0000, LENGTH = 0x0000
  tinyram (wx) : ORIGIN = 0x0000, LENGTH = 0x0000
  usbram (wx) : ORIGIN = 0x0000, LENGTH = 0x0000
  far_rom : ORIGIN = 0x00000000, LENGTH = 0x00000000
}
REGION_ALIAS("REGION_TEXT", rom);
REGION_ALIAS("REGION_DATA", ram);
REGION_ALIAS("REGION_FAR_ROM", far_rom); /* Legacy name, no longer used */
REGION_ALIAS("REGION_FAR_TEXT", far_rom);
REGION_ALIAS("REGION_FAR_DATA", ram2);
/* INCLUDE memory.x end */

/*INCLUDE periph.x begin */
/* This file supports MSP430FR2433 devices. */
/* Version: 1.193 */

/************************************************************
* STANDARD BITS
************************************************************/
/************************************************************
* STATUS REGISTER BITS
************************************************************/
/************************************************************
* CPU
************************************************************/
/************************************************************
* PERIPHERAL FILE MAP
************************************************************/
/************************************************************
* ADC
************************************************************/
__ADCCTL0 = 0x0700;
__ADCCTL0_L = 0x0700;
__ADCCTL0_H = 0x0701;
__ADCCTL1 = 0x0702;
__ADCCTL1_L = 0x0702;
__ADCCTL1_H = 0x0703;
__ADCCTL2 = 0x0704;
__ADCCTL2_L = 0x0704;
__ADCCTL2_H = 0x0705;
__ADCLO = 0x0706;
__ADCLO_L = 0x0706;
__ADCLO_H = 0x0707;
__ADCHI = 0x0708;
__ADCHI_L = 0x0708;
__ADCHI_H = 0x0709;
__ADCMCTL0 = 0x070A;
__ADCMCTL0_L = 0x070A;
__ADCMCTL0_H = 0x070B;
__ADCMEM0 = 0x0712;
__ADCMEM0_L = 0x0712;
__ADCMEM0_H = 0x0713;
__ADCIE = 0x071A;
__ADCIE_L = 0x071A;
__ADCIE_H = 0x071B;
__ADCIFG = 0x071C;
__ADCIFG_L = 0x071C;
__ADCIFG_H = 0x071D;
__ADCIV = 0x071E;
__ADCIV_L = 0x071E;
__ADCIV_H = 0x071F;
/*************************************************************
* Backup Memory Module
*************************************************************/
__BAKMEM0 = 0x0660;
__BAKMEM0_L = 0x0660;
__BAKMEM0_H = 0x0661;
__BAKMEM1 = 0x0662;
__BAKMEM1_L = 0x0662;
__BAKMEM1_H = 0x0663;
__BAKMEM2 = 0x0664;
__BAKMEM2_L = 0x0664;
__BAKMEM2_H = 0x0665;
__BAKMEM3 = 0x0666;
__BAKMEM3_L = 0x0666;
__BAKMEM3_H = 0x0667;
__BAKMEM4 = 0x0668;
__BAKMEM4_L = 0x0668;
__BAKMEM4_H = 0x0669;
__BAKMEM5 = 0x066A;
__BAKMEM5_L = 0x066A;
__BAKMEM5_H = 0x066B;
__BAKMEM6 = 0x066C;
__BAKMEM6_L = 0x066C;
__BAKMEM6_H = 0x066D;
__BAKMEM7 = 0x066E;
__BAKMEM7_L = 0x066E;
__BAKMEM7_H = 0x066F;
__BAKMEM8 = 0x0670;
__BAKMEM8_L = 0x0670;
__BAKMEM8_H = 0x0671;
__BAKMEM9 = 0x0672;
__BAKMEM9_L = 0x0672;
__BAKMEM9_H = 0x0673;
__BAKMEM10 = 0x0674;
__BAKMEM10_L = 0x0674;
__BAKMEM10_H = 0x0675;
__BAKMEM11 = 0x0676;
__BAKMEM11_L = 0x0676;
__BAKMEM11_H = 0x0677;
__BAKMEM12 = 0x0678;
__BAKMEM12_L = 0x0678;
__BAKMEM12_H = 0x0679;
__BAKMEM13 = 0x067A;
__BAKMEM13_L = 0x067A;
__BAKMEM13_H = 0x067B;
__BAKMEM14 = 0x067C;
__BAKMEM14_L = 0x067C;
__BAKMEM14_H = 0x067D;
__BAKMEM15 = 0x067E;
__BAKMEM15_L = 0x067E;
__BAKMEM15_H = 0x067F;
/*************************************************************
* CRC Module
*************************************************************/
__CRCDI = 0x01C0;
__CRCDI_L = 0x01C0;
__CRCDI_H = 0x01C1;
__CRCDIRB = 0x01C2;
__CRCDIRB_L = 0x01C2;
__CRCDIRB_H = 0x01C3;
__CRCINIRES = 0x01C4;
__CRCINIRES_L = 0x01C4;
__CRCINIRES_H = 0x01C5;
__CRCRESR = 0x01C6;
__CRCRESR_L = 0x01C6;
__CRCRESR_H = 0x01C7;
/************************************************************
* CLOCK SYSTEM CONTROL
************************************************************/
__CSCTL0 = 0x0180;
__CSCTL0_L = 0x0180;
__CSCTL0_H = 0x0181;
__CSCTL1 = 0x0182;
__CSCTL1_L = 0x0182;
__CSCTL1_H = 0x0183;
__CSCTL2 = 0x0184;
__CSCTL2_L = 0x0184;
__CSCTL2_H = 0x0185;
__CSCTL3 = 0x0186;
__CSCTL3_L = 0x0186;
__CSCTL3_H = 0x0187;
__CSCTL4 = 0x0188;
__CSCTL4_L = 0x0188;
__CSCTL4_H = 0x0189;
__CSCTL5 = 0x018A;
__CSCTL5_L = 0x018A;
__CSCTL5_H = 0x018B;
__CSCTL6 = 0x018C;
__CSCTL6_L = 0x018C;
__CSCTL6_H = 0x018D;
__CSCTL7 = 0x018E;
__CSCTL7_L = 0x018E;
__CSCTL7_H = 0x018F;
__CSCTL8 = 0x0190;
__CSCTL8_L = 0x0190;
__CSCTL8_H = 0x0191;
/*************************************************************
* FRAM Memory
*************************************************************/
__FRCTL0 = 0x01A0;
__FRCTL0_L = 0x01A0;
__FRCTL0_H = 0x01A1;
__GCCTL0 = 0x01A4;
__GCCTL0_L = 0x01A4;
__GCCTL0_H = 0x01A5;
__GCCTL1 = 0x01A6;
__GCCTL1_L = 0x01A6;
__GCCTL1_H = 0x01A7;
/************************************************************
* HARDWARE MULTIPLIER 32Bit
************************************************************/
__MPY = 0x04C0;
__MPY_L = 0x04C0;
__MPY_H = 0x04C1;
__MPYS = 0x04C2;
__MPYS_L = 0x04C2;
__MPYS_H = 0x04C3;
__MAC = 0x04C4;
__MAC_L = 0x04C4;
__MAC_H = 0x04C5;
__MACS = 0x04C6;
__MACS_L = 0x04C6;
__MACS_H = 0x04C7;
__OP2 = 0x04C8;
__OP2_L = 0x04C8;
__OP2_H = 0x04C9;
__RESLO = 0x04CA;
__RESLO_L = 0x04CA;
__RESLO_H = 0x04CB;
__RESHI = 0x04CC;
__RESHI_L = 0x04CC;
__RESHI_H = 0x04CD;
__SUMEXT = 0x04CE;
__SUMEXT_L = 0x04CE;
__SUMEXT_H = 0x04CF;
__MPY32L = 0x04D0;
__MPY32L_L = 0x04D0;
__MPY32L_H = 0x04D1;
__MPY32H = 0x04D2;
__MPY32H_L = 0x04D2;
__MPY32H_H = 0x04D3;
__MPYS32L = 0x04D4;
__MPYS32L_L = 0x04D4;
__MPYS32L_H = 0x04D5;
__MPYS32H = 0x04D6;
__MPYS32H_L = 0x04D6;
__MPYS32H_H = 0x04D7;
__MAC32L = 0x04D8;
__MAC32L_L = 0x04D8;
__MAC32L_H = 0x04D9;
__MAC32H = 0x04DA;
__MAC32H_L = 0x04DA;
__MAC32H_H = 0x04DB;
__MACS32L = 0x04DC;
__MACS32L_L = 0x04DC;
__MACS32L_H = 0x04DD;
__MACS32H = 0x04DE;
__MACS32H_L = 0x04DE;
__MACS32H_H = 0x04DF;
__OP2L = 0x04E0;
__OP2L_L = 0x04E0;
__OP2L_H = 0x04E1;
__OP2H = 0x04E2;
__OP2H_L = 0x04E2;
__OP2H_H = 0x04E3;
__RES0 = 0x04E4;
__RES0_L = 0x04E4;
__RES0_H = 0x04E5;
__RES1 = 0x04E6;
__RES1_L = 0x04E6;
__RES1_H = 0x04E7;
__RES2 = 0x04E8;
__RES2_L = 0x04E8;
__RES2_H = 0x04E9;
__RES3 = 0x04EA;
__RES3_L = 0x04EA;
__RES3_H = 0x04EB;
__MPY32CTL0 = 0x04EC;
__MPY32CTL0_L = 0x04EC;
__MPY32CTL0_H = 0x04ED;
/************************************************************
* PMM - Power Management System for FR2xx/FR4xx
************************************************************/
__PMMCTL0 = 0x0120;
__PMMCTL0_L = 0x0120;
__PMMCTL0_H = 0x0121;
__PMMCTL1 = 0x0122;
__PMMCTL1_L = 0x0122;
__PMMCTL1_H = 0x0123;
__PMMCTL2 = 0x0124;
__PMMCTL2_L = 0x0124;
__PMMCTL2_H = 0x0125;
__PMMIFG = 0x012A;
__PMMIFG_L = 0x012A;
__PMMIFG_H = 0x012B;
__PMMIE = 0x012E;
__PMMIE_L = 0x012E;
__PMMIE_H = 0x012F;
__PM5CTL0 = 0x0130;
__PM5CTL0_L = 0x0130;
__PM5CTL0_H = 0x0131;
/************************************************************
* DIGITAL I/O Port1/2 Pull up / Pull down Resistors
************************************************************/
__PAIN = 0x0200;
__PAIN_L = 0x0200;
__PAIN_H = 0x0201;
__PAOUT = 0x0202;
__PAOUT_L = 0x0202;
__PAOUT_H = 0x0203;
__PADIR = 0x0204;
__PADIR_L = 0x0204;
__PADIR_H = 0x0205;
__PAREN = 0x0206;
__PAREN_L = 0x0206;
__PAREN_H = 0x0207;
__PASEL0 = 0x020A;
__PASEL0_L = 0x020A;
__PASEL0_H = 0x020B;
__PASEL1 = 0x020C;
__PASEL1_L = 0x020C;
__PASEL1_H = 0x020D;
__PAIES = 0x0218;
__PAIES_L = 0x0218;
__PAIES_H = 0x0219;
__PAIE = 0x021A;
__PAIE_L = 0x021A;
__PAIE_H = 0x021B;
__PAIFG = 0x021C;
__PAIFG_L = 0x021C;
__PAIFG_H = 0x021D;
__P1IV = 0x020E;
__P2IV = 0x021E;
/************************************************************
* DIGITAL I/O Port3 Pull up / Pull down Resistors
************************************************************/
__PBIN = 0x0220;
__PBIN_L = 0x0220;
__PBIN_H = 0x0221;
__PBOUT = 0x0222;
__PBOUT_L = 0x0222;
__PBOUT_H = 0x0223;
__PBDIR = 0x0224;
__PBDIR_L = 0x0224;
__PBDIR_H = 0x0225;
__PBREN = 0x0226;
__PBREN_L = 0x0226;
__PBREN_H = 0x0227;
__PBSEL0 = 0x022A;
__PBSEL0_L = 0x022A;
__PBSEL0_H = 0x022B;
__PBSEL1 = 0x022C;
__PBSEL1_L = 0x022C;
__PBSEL1_H = 0x022D;
/************************************************************
* Real-Time Clock (RTC) Counter
************************************************************/
__RTCCTL = 0x0300;
__RTCCTL_L = 0x0300;
__RTCCTL_H = 0x0301;
__RTCIV = 0x0304;
__RTCIV_L = 0x0304;
__RTCIV_H = 0x0305;
__RTCMOD = 0x0308;
__RTCMOD_L = 0x0308;
__RTCMOD_H = 0x0309;
__RTCCNT = 0x030C;
__RTCCNT_L = 0x030C;
__RTCCNT_H = 0x030D;
/************************************************************
* SFR - Special Function Register Module
************************************************************/
__SFRIE1 = 0x0100;
__SFRIE1_L = 0x0100;
__SFRIE1_H = 0x0101;
__SFRIFG1 = 0x0102;
__SFRIFG1_L = 0x0102;
__SFRIFG1_H = 0x0103;
__SFRRPCR = 0x0104;
__SFRRPCR_L = 0x0104;
__SFRRPCR_H = 0x0105;
/************************************************************
* SYS - System Module
************************************************************/
__SYSCTL = 0x0140;
__SYSCTL_L = 0x0140;
__SYSCTL_H = 0x0141;
__SYSBSLC = 0x0142;
__SYSBSLC_L = 0x0142;
__SYSBSLC_H = 0x0143;
__SYSJMBC = 0x0146;
__SYSJMBC_L = 0x0146;
__SYSJMBC_H = 0x0147;
__SYSJMBI0 = 0x0148;
__SYSJMBI0_L = 0x0148;
__SYSJMBI0_H = 0x0149;
__SYSJMBI1 = 0x014A;
__SYSJMBI1_L = 0x014A;
__SYSJMBI1_H = 0x014B;
__SYSJMBO0 = 0x014C;
__SYSJMBO0_L = 0x014C;
__SYSJMBO0_H = 0x014D;
__SYSJMBO1 = 0x014E;
__SYSJMBO1_L = 0x014E;
__SYSJMBO1_H = 0x014F;
__SYSBERRIV = 0x0158;
__SYSBERRIV_L = 0x0158;
__SYSBERRIV_H = 0x0159;
__SYSUNIV = 0x015A;
__SYSUNIV_L = 0x015A;
__SYSUNIV_H = 0x015B;
__SYSSNIV = 0x015C;
__SYSSNIV_L = 0x015C;
__SYSSNIV_H = 0x015D;
__SYSRSTIV = 0x015E;
__SYSRSTIV_L = 0x015E;
__SYSRSTIV_H = 0x015F;
__SYSCFG0 = 0x0160;
__SYSCFG0_L = 0x0160;
__SYSCFG0_H = 0x0161;
__SYSCFG1 = 0x0162;
__SYSCFG1_L = 0x0162;
__SYSCFG1_H = 0x0163;
__SYSCFG2 = 0x0164;
__SYSCFG2_L = 0x0164;
__SYSCFG2_H = 0x0165;
/************************************************************
* Timer0_A3
************************************************************/
__TA0CTL = 0x0380;
__TA0CCTL0 = 0x0382;
__TA0CCTL1 = 0x0384;
__TA0CCTL2 = 0x0386;
__TA0R = 0x0390;
__TA0CCR0 = 0x0392;
__TA0CCR1 = 0x0394;
__TA0CCR2 = 0x0396;
__TA0IV = 0x03AE;
__TA0EX0 = 0x03A0;
/************************************************************
* Timer1_A3
************************************************************/
__TA1CTL = 0x03C0;
__TA1CCTL0 = 0x03C2;
__TA1CCTL1 = 0x03C4;
__TA1CCTL2 = 0x03C6;
__TA1R = 0x03D0;
__TA1CCR0 = 0x03D2;
__TA1CCR1 = 0x03D4;
__TA1CCR2 = 0x03D6;
__TA1IV = 0x03EE;
__TA1EX0 = 0x03E0;
/************************************************************
* Timer2_A2
************************************************************/
__TA2CTL = 0x0400;
__TA2CCTL0 = 0x0402;
__TA2CCTL1 = 0x0404;
__TA2R = 0x0410;
__TA2CCR0 = 0x0412;
__TA2CCR1 = 0x0414;
__TA2IV = 0x042E;
__TA2EX0 = 0x0420;
/************************************************************
* Timer3_A2
************************************************************/
__TA3CTL = 0x0440;
__TA3CCTL0 = 0x0442;
__TA3CCTL1 = 0x0444;
__TA3R = 0x0450;
__TA3CCR0 = 0x0452;
__TA3CCR1 = 0x0454;
__TA3IV = 0x046E;
__TA3EX0 = 0x0460;
/************************************************************
* USCI A0
************************************************************/
__UCA0CTLW0 = 0x0500;
__UCA0CTLW0_L = 0x0500;
__UCA0CTLW0_H = 0x0501;
__UCA0CTLW1 = 0x0502;
__UCA0CTLW1_L = 0x0502;
__UCA0CTLW1_H = 0x0503;
__UCA0BRW = 0x0506;
__UCA0BRW_L = 0x0506;
__UCA0BRW_H = 0x0507;
__UCA0MCTLW = 0x0508;
__UCA0MCTLW_L = 0x0508;
__UCA0MCTLW_H = 0x0509;
__UCA0STATW = 0x050A;
__UCA0RXBUF = 0x050C;
__UCA0RXBUF_L = 0x050C;
__UCA0RXBUF_H = 0x050D;
__UCA0TXBUF = 0x050E;
__UCA0TXBUF_L = 0x050E;
__UCA0TXBUF_H = 0x050F;
__UCA0ABCTL = 0x0510;
__UCA0IRCTL = 0x0512;
__UCA0IRCTL_L = 0x0512;
__UCA0IRCTL_H = 0x0513;
__UCA0IE = 0x051A;
__UCA0IE_L = 0x051A;
__UCA0IE_H = 0x051B;
__UCA0IFG = 0x051C;
__UCA0IFG_L = 0x051C;
__UCA0IFG_H = 0x051D;
__UCA0IV = 0x051E;
/************************************************************
* USCI A1
************************************************************/
__UCA1CTLW0 = 0x0520;
__UCA1CTLW0_L = 0x0520;
__UCA1CTLW0_H = 0x0521;
__UCA1CTLW1 = 0x0522;
__UCA1CTLW1_L = 0x0522;
__UCA1CTLW1_H = 0x0523;
__UCA1BRW = 0x0526;
__UCA1BRW_L = 0x0526;
__UCA1BRW_H = 0x0527;
__UCA1MCTLW = 0x0528;
__UCA1MCTLW_L = 0x0528;
__UCA1MCTLW_H = 0x0529;
__UCA1STATW = 0x052A;
__UCA1RXBUF = 0x052C;
__UCA1RXBUF_L = 0x052C;
__UCA1RXBUF_H = 0x052D;
__UCA1TXBUF = 0x052E;
__UCA1TXBUF_L = 0x052E;
__UCA1TXBUF_H = 0x052F;
__UCA1ABCTL = 0x0530;
__UCA1IRCTL = 0x0532;
__UCA1IRCTL_L = 0x0532;
__UCA1IRCTL_H = 0x0533;
__UCA1IE = 0x053A;
__UCA1IE_L = 0x053A;
__UCA1IE_H = 0x053B;
__UCA1IFG = 0x053C;
__UCA1IFG_L = 0x053C;
__UCA1IFG_H = 0x053D;
__UCA1IV = 0x053E;
/************************************************************
* USCI B0
************************************************************/
__UCB0CTLW0 = 0x0540;
__UCB0CTLW0_L = 0x0540;
__UCB0CTLW0_H = 0x0541;
__UCB0CTLW1 = 0x0542;
__UCB0CTLW1_L = 0x0542;
__UCB0CTLW1_H = 0x0543;
__UCB0BRW = 0x0546;
__UCB0BRW_L = 0x0546;
__UCB0BRW_H = 0x0547;
__UCB0STATW = 0x0548;
__UCB0STATW_L = 0x0548;
__UCB0STATW_H = 0x0549;
__UCB0TBCNT = 0x054A;
__UCB0TBCNT_L = 0x054A;
__UCB0TBCNT_H = 0x054B;
__UCB0RXBUF = 0x054C;
__UCB0RXBUF_L = 0x054C;
__UCB0RXBUF_H = 0x054D;
__UCB0TXBUF = 0x054E;
__UCB0TXBUF_L = 0x054E;
__UCB0TXBUF_H = 0x054F;
__UCB0I2COA0 = 0x0554;
__UCB0I2COA0_L = 0x0554;
__UCB0I2COA0_H = 0x0555;
__UCB0I2COA1 = 0x0556;
__UCB0I2COA1_L = 0x0556;
__UCB0I2COA1_H = 0x0557;
__UCB0I2COA2 = 0x0558;
__UCB0I2COA2_L = 0x0558;
__UCB0I2COA2_H = 0x0559;
__UCB0I2COA3 = 0x055A;
__UCB0I2COA3_L = 0x055A;
__UCB0I2COA3_H = 0x055B;
__UCB0ADDRX = 0x055C;
__UCB0ADDRX_L = 0x055C;
__UCB0ADDRX_H = 0x055D;
__UCB0ADDMASK = 0x055E;
__UCB0ADDMASK_L = 0x055E;
__UCB0ADDMASK_H = 0x055F;
__UCB0I2CSA = 0x0560;
__UCB0I2CSA_L = 0x0560;
__UCB0I2CSA_H = 0x0561;
__UCB0IE = 0x056A;
__UCB0IE_L = 0x056A;
__UCB0IE_H = 0x056B;
__UCB0IFG = 0x056C;
__UCB0IFG_L = 0x056C;
__UCB0IFG_H = 0x056D;
__UCB0IV = 0x056E;
/************************************************************
* WATCHDOG TIMER A
************************************************************/
__WDTCTL = 0x01CC;
__WDTCTL_L = 0x01CC;
__WDTCTL_H = 0x01CD;
/************************************************************
* TLV Descriptors
************************************************************/
/************************************************************
* Interrupt Vectors (offset from 0xFF80 + 0x10 for Password)
************************************************************/
/************************************************************
* End of Modules
************************************************************/
/*INCLUDE periph.x end */

SECTIONS
{
  /* Read-only sections, merged into text segment. */
  .hash : { *(.hash) }
  .dynsym : { *(.dynsym) }
  .dynstr : { *(.dynstr) }
  .gnu.version : { *(.gnu.version) }
  .gnu.version_d : { *(.gnu.version_d) }
  .gnu.version_r : { *(.gnu.version_r) }
  .rel.init : { *(.rel.init) }
  .rela.init : { *(.rela.init) }
  .rel.fini : { *(.rel.fini) }
  .rela.fini : { *(.rela.fini) }
  .rel.text : { *(.rel.text .rel.text.* .rel.gnu.linkonce.t.*) }
  .rela.text : { *(.rela.text .rela.text.* .rela.gnu.linkonce.t.*) }
  .rel.rodata : { *(.rel.rodata .rel.rodata.* .rel.gnu.linkonce.r.*) }
  .rela.rodata : { *(.rela.rodata .rela.rodata.* .rela.gnu.linkonce.r.*) }
  .rel.data : { *(.rel.data .rel.data.* .rel.gnu.linkonce.d.*) }
  .rela.data : { *(.rela.data .rela.data.* .rela.gnu.linkonce.d.*) }
  .rel.bss : { *(.rel.bss .rel.bss.* .rel.gnu.linkonce.b.*) }
  .rela.bss : { *(.rela.bss .rela.bss.* .rela.gnu.linkonce.b.*) }
  .rel.ctors : { *(.rel.ctors) }
  .rela.ctors : { *(.rela.ctors) }
  .rel.dtors : { *(.rel.dtors) }
  .rela.dtors : { *(.rela.dtors) }
  .rel.got : { *(.rel.got) }
  .rela.got : { *(.rela.got) }
  .rel.plt : { *(.rel.plt) }
  .rela.plt : { *(.rela.plt) }
  .text :
  {
     . = ALIGN(2);
     KEEP(*(.init .init.*))
     KEEP(*(.init0)) /* Start here after reset. */
     KEEP(*(.init1)) /* User definable. */
     KEEP(*(.init2)) /* Initialize stack. */
     KEEP(*(.init3)) /* Initialize hardware, user definable. */
     KEEP(*(.init4)) /* Copy data to .data, clear bss. */
     KEEP(*(.init5)) /* User definable. */
     KEEP(*(.init6)) /* C++ constructors. */
     KEEP(*(.init7)) /* User definable. */
     KEEP(*(.init8)) /* User definable. */
     KEEP(*(.init9)) /* Call main(). */
     KEEP(*(.fini9)) /* Falls into here after main(). User definable. */
     KEEP(*(.fini8)) /* User definable. */
     KEEP(*(.fini7)) /* User definable. */
     KEEP(*(.fini6)) /* C++ destructors. */
     KEEP(*(.fini5)) /* User definable. */
     KEEP(*(.fini4)) /* User definable. */
     KEEP(*(.fini3)) /* User definable. */
     KEEP(*(.fini2)) /* User definable. */
     KEEP(*(.fini1)) /* User definable. */
     KEEP(*(.fini0)) /* Infinite loop after program termination. */
     KEEP(*(.fini .fini.*))
     . = ALIGN(2);
     __ctors_start = . ;
     KEEP(*(.ctors))
     __ctors_end = . ;
     __dtors_start = . ;
     KEEP(*(.dtors))
     __dtors_end = . ;
     . = ALIGN(2);
    *(.text .text.* .gnu.linkonce.t.*)
     . = ALIGN(2);
  } > REGION_TEXT
  .rodata :
  {
     . = ALIGN(2);
    *(.rodata .rodata.* .gnu.linkonce.r.*)
     . = ALIGN(2);
  } > REGION_TEXT
   _etext = .; /* Past last read-only (loadable) segment */
  .data :
  {
     . = ALIGN(2);
     PROVIDE (__data_start = .) ;
    *(.data .data.* .gnu.linkonce.d.*)
     . = ALIGN(2);
     _edata = . ; /* Past last read-write (loadable) segment */
  } > REGION_DATA AT > REGION_TEXT
   PROVIDE (__data_load_start = LOADADDR(.data) );
   PROVIDE (__data_size = SIZEOF(.data) );
  .bss :
  {
     PROVIDE (__bss_start = .) ;
    *(.bss .bss.*)
    *(COMMON)
     . = ALIGN(2);
     PROVIDE (__bss_end = .) ;
  } > REGION_DATA
   PROVIDE (__bss_size = SIZEOF(.bss) );
  .noinit :
  {
     PROVIDE (__noinit_start = .) ;
    *(.noinit .noinit.*)
     . = ALIGN(2);
     PROVIDE (__noinit_end = .) ;
  } > REGION_DATA
   . = ALIGN(2);
   _end = . ; /* Past last write (loadable) segment */
  .infomem :
  {
    *(.infomem)
     . = ALIGN(2);
    *(.infomem.*)
  } > infomem
  .infomemnobits :
  {
    *(.infomemnobits)
     . = ALIGN(2);
    *(.infomemnobits.*)
  } > infomem
  .infoa :
  {
    *(.infoa .infoa.*)
  } > infoa
  .infob :
  {
    *(.infob .infob.*)
  } > infob
  .infoc :
  {
    *(.infoc .infoc.*)
  } > infoc
  .infod :
  {
    *(.infod .infod.*)
  } > infod
  .vectors :
  {
     PROVIDE (__vectors_start = .) ;
    KEEP(*(.vectors*))
     _vectors_end = . ;
  } > vectors
  .fartext :
  {
     . = ALIGN(2);
    *(.fartext)
     . = ALIGN(2);
    *(.fartext.*)
     _efartext = .;
  } > REGION_FAR_ROM
  /* Stabs for profiling information*/
  .profiler 0 : { *(.profiler) }
  /* Stabs debugging sections. */
  .stab 0 : { *(.stab) }
  .stabstr 0 : { *(.stabstr) }
  .stab.excl 0 : { *(.stab.excl) }
  .stab.exclstr 0 : { *(.stab.exclstr) }
  .stab.index 0 : { *(.stab.index) }
  .stab.indexstr 0 : { *(.stab.indexstr) }
  .comment 0 : { *(.comment) }
  /* DWARF debug sections.
     Symbols in the DWARF debugging sections are relative to the beginning
     of the section so we begin them at 0. */
  /* DWARF 1 */
  .debug 0 : { *(.debug) }
  .line 0 : { *(.line) }
  /* GNU DWARF 1 extensions */
  .debug_srcinfo 0 : { *(.debug_srcinfo) }
  .debug_sfnames 0 : { *(.debug_sfnames) }
  /* DWARF 1.1 and DWARF 2 */
  .debug_aranges 0 : { *(.debug_aranges) }
  .debug_pubnames 0 : { *(.debug_pubnames) }
  /* DWARF 2 */
  .debug_info 0 : { *(.debug_info) *(.gnu.linkonce.wi.*) }
  .debug_abbrev 0 : { *(.debug_abbrev) }
  .debug_line 0 : { *(.debug_line) }
  .debug_frame 0 : { *(.debug_frame) }
  .debug_str 0 : { *(.debug_str) }
  .debug_loc 0 : { *(.debug_loc) }
  .debug_macinfo 0 : { *(.debug_macinfo) }
  /* DWARF 3 */
  .debug_pubtypes 0 : { *(.debug_pubtypes) }
  .debug_ranges 0 : { *(.debug_ranges) }
   PROVIDE (__stack = ORIGIN(ram) + LENGTH(ram));
   PROVIDE (__data_start_rom = _etext);
   PROVIDE (__data_end_rom = _etext + SIZEOF (.data));
}